## Slide 1: Chapter Three
Hardware

## Slide 2: Computer Hierarchy
Mainframes -- the first. Used for business
Supercomputers -- the largest, very complex
Minicomputers -- the first effort to achieve reduced size (middle-ranged)
Microcomputers -- made possible by microprocessor
  PC/MAC-- used by one person, or by a few people in the same area
  Workstations, laptops, netbooks, tablets/iPads, smartphone

## Slide 3: Servers, Mainframes, and Supercomputers
Notes: Servers, Mainframes, and Supercomputers

## Slide 4: Hardware consists of:
Central processing unit (CPU) manipulates the data and controls the tasks performed by the other components.
Primary storage internal to the CPU; temporarily stores data and program instructions during processing.
Secondary storage external to the CPU; stores data and programs for future use.
Input technologies
Output technologies
Communication technologies provide for the flow of data from external computer networks (e.g. the Internet and intranets) to the CPU, and from the CPU to computer networks.
Notes: Central processing unit (CPU) manipulates the data and controls the tasks performed by the other components.
Primary storage internal to the CPU; temporarily stores data and program instructions during processing.
Secondary storage external to the CPU; stores data and programs for future use.
Input technologies accept data and instructions and convert them to a form that the computer can understand.
Output technologies present data and information in a form people can understand.
Communication technologies provide for the flow of data from external computer networks (e.g. the Internet and intranets) to the CPU, and from the CPU to computer networks.

## Slide 5: Computer Memory
Two basic categories of computer memory:
  Primary Storage
  Secondary Storage
Memory Capacity:
  Bit
  Byte
Notes:   Primary Storage stores small amounts of data and information that will be immediately used by the CPU.
  Secondary Storage stores much larger amounts of data and information (an entire software program, for example) for extended periods of time.
  Bit: Short for binary digit (0s and 1s), the only data that a CPU can process.
  Byte: An 8-bit string of data, needed to represent any one alphanumeric character or simple mathematical operation.

## Slide 6: Hierarchy of Memory Capacity
Kilobyte
Megabyte
Gigabyte
Terabyte
Petabyte
Exabyte
Zettabyte
Notes: Kilobyte (KB): approximately one thousand bytes.
Megabyte (MB): approximately one million bytes (1,048,576 bytes, or 1,024 x 1,024).
Gigabyte (GB): actually 1,073,741,824 bytes (1,024 x 1,024 x 1,024 bytes).
Terabyte: One trillion bytes.
Petabyte: One thousand terabytes.
Exabyte: One thousand petabytes.
Zettabyte: one thousand exabytes.

## Slide 7: The Computer Bytes
Computers deal in either
  ASCII- American Standard Code for Information Interchange (7 bits with 1 parity bit)
    EX. A = 01000001
  EBCDIC- Extended Binary Coded Decimal Interchange Code an 8-bit code used in IBM
    EX. A = 11000001

## Slide 8: Understanding Bits and Bytes

## Slide 9: Converting to Binary

## Slide 10: Internal workings of personal computer
RAM
Hard disk drive
Floppy disk drive
CPU board with fan

## Slide 11: The Computer Schematic

## Slide 12: Improving Performance
There are three main ways to accomplish this
  word length -the number of bits that can be processed together as a unit
    current computers are either 32 or 64bit
  bus width - the amount of bits that can be transferred within the computer at any given computer interrupt
    bus width range also varies
  clock speed
  RISC- reduced instruction set computing
  MMX- MultiMedia eXtension

## Slide 13: Advances in Microprocessor Design
Moore’s Law: microprocessor complexity would double every two years.
Notes: Moore’s Law is that microprocessor complexity would double every two years as a result of the following changes:
  --Increasing miniaturization of transistors.
  --Making the physical layout of the chip’s components as compact and efficient as possible.
  --Using materials for the chip that improve the conductivity (flow) of electricity.
  --Targeting the amount of basic instructions programmed into the chip.

## Slide 14: Server Farms, Data Centers, and Green Computing
This section provides an overview of what the computer industry and various organizations are doing to meet their computing needs in a more efficient and environmentally friendly manner
Notes: Server Farms, Data Centers, and Green Computing
This section provides an overview of what the computer industry and various organizations are doing to meet their computing needs in a more efficient and environmentally friendly manner

## Slide 15: Server Farms
Server farm: a room used to house a large number of servers
  Access to the machines can be controlled and authorized support personnel can more easily manage and maintain the servers
Virtual server: a method of logically dividing the resources of a single physical server to create multiple logical servers
  Each logical server acts as its own dedicated machine
Blade server: a server that houses many individual computer motherboards
  Include one or more processors, computer memory, computer storage, and computer network connections
  Share a common power supply and air-cooling source within a single chassis
Notes: Server Farms
Server farm: a room used to house a large number of servers
  Access to the machines can be controlled and authorized support personnel can more easily manage and maintain the servers
Virtual server: a method of logically dividing the resources of a single physical server to create multiple logical servers
  Each logical server acts as its own dedicated machine
Blade server: a server that houses many individual computer motherboards
  Include one or more processors, computer memory, computer storage, and computer network connections
  Share a common power supply and air-cooling source within a single chassis

## Slide 16: Server Farms
Notes: Server Farms

## Slide 17: Data Center
Data center
  A climate-and-access-controlled building or a set of buildings that houses the computer hardware that delivers an organization’s data and information services
Factors driving growth in data centers:
  Demand for additional computing capacity
  Need for additional storage capacity
  Some organizations are consolidating data centers from many locations down to just a few locations
Notes: Data Center
Data center
  A climate-and-access-controlled building or a set of buildings that houses the computer hardware that delivers an organization’s data and information services
Factors driving growth in data centers:
  Demand for additional computing capacity
  Need for additional storage capacity
  Some organizations are consolidating data centers from many locations down to just a few locations

## Slide 18: Data Center
Notes: Data Center

## Slide 19: Data Center
Construction Considerations
  More efficient operation and reduced energy for processing and cooling
    Modular design
    Location: areas with milder climates and lower energy rates and land costs
  Ability to absorb the impact of a disaster (e.g., hurricane, earthquake, terrorism attack, or war) and quickly restore services
Notes: Data Center
Construction Considerations
  More efficient operation and reduced energy for processing and cooling
    Modular design
    Location: areas with milder climates and lower energy rates and land costs
  Ability to absorb the impact of a disaster (e.g., hurricane, earthquake, terrorism attack, or war) and quickly restore services

## Slide 20: Green Computing
A program concerned with the efficient and environmentally responsible design, manufacture, operation, and disposal of IS-related products
Goals
  Reduce the use of hazardous material
  Allow companies to lower their power-related costs
  Enable safe disposal or recycling of equipment
Notes: Green Computing
A program concerned with the efficient and environmentally responsible design, manufacture, operation, and disposal of IS-related products
Goals
  Reduce the use of hazardous material
  Allow companies to lower their power-related costs
  Enable safe disposal or recycling of equipment

## Slide 21: Green Computing
Electronic Product Environmental Assessment Tool (EPEAT)
  A system that enables purchasers to evaluate, compare, and select electronic products based on a total of 51 environmental criteria
Notes: Green Computing
Electronic Product Environmental Assessment Tool (EPEAT)
  A system that enables purchasers to evaluate, compare, and select electronic products based on a total of 51 environmental criteria

## Slide 22: Strategic Hardware Issues
How do organizations keep up with the rapid price and performance advancements in hardware?
How often should an organization upgrade its computers and storage systems?
Will upgrades increase personal and organizational productivity?

## Slide 23: Strategic Hardware Issues
How can organizations measure such increase?
How should organizations determine the need for new hardware infrastructures?
How do organizations manage employees who can “work from anywhere?”